3D Models

---
Recap: shape and material – 3D object
- Representing a real world phenomena, and in order to create objects in a 3D scene, requires a way of representing:
  - Shape
  - Appearance
<IMAGE: shape vs material intuition>

---
Appearance of 3D object
Material representation

---
Observation
- Modeling materials begins with observation to understand what makes each material look different than other materials
- We don’t want to observe just appearance (like artists do). We want to observe characteristics which are responsible for object appearance:
  - Shape
  - Illumination
  - Sensor/Perception
  - Material
<BOOK: DIGITAL MODELING OF MATERIAL APPERANCE (J. DORSEY)>
PDF COURSE: Digital modeling of the appearance of materials
<EXAMPLES: CHARACTERISTICS RESPONSIBLE FOR APPEARANCE>

---
Classifying materials
- Classifying materials enables us to understand which characteristics are needed to be modeled in order to obtain required appearance. We can classify any material by following variations:
  - Spectral
  - Directional
  - Spatial

---
Examples of different materials
- TODO
- PDF COURSE: Digital modeling of the appearance of materials

---
Foundations of materials: physics
- Material defines interaction of light with objects
  - Light is electromagnetic wave (visible part of spectrum). In computer graphics we work with geometrical optics which is approximation and light is represented using rays.
- Light falling on objects, based on index of refraction will*:
  - Absorb
  - Scatter
- Homogeneous material: light travels on a straight line, it can only be absorbed, meaning that direction is same, but intensity might be lower.
  - In transparent material (e.g. glass or water) light propagates in straight line – no scattering (scattering happens on interface – boundary between materials). Also, low absorption of light.
  - Homogeneous material with higher absorption will attenuate light traveling through it or completely absorb it if distance is large – but the direction will not change! An example is water over larger distances.
  - Note that also light can be selectively absorbed, meaning that it changes color (alongside intensity).
- Heterogeneous material: light is scattered → direction of light is changed but not necessary the intensity
  - Light can scatter in all directions, mostly non-uniformly: forward or back scattering
  - Translucent or opaque materials are examples of heterogeneous materials → light is scattered so much that we can not see (clearly) through the object
  - Longer distances cause more scattering, but not necessary more absorption (e.g., clean air)
<IMAGES OF REAL WORLD OBJECT SHOWING THOSE CHARACTERISTICS>
* Light interaction with matter (on geometrical optics) is determined by index of refraction – complex number. Real part determines speed of light, imaginary part determines absorption.Constant index of refraction is present in homogeneous materials where index of refraction is constant. For such materials, only absorption happens. Varying index of refraction is present in heterogeneous materials causing scattering (next to absorption).

---
Reflection on optically flat surfaces
- Light interaction with matter can be described with Maxwell’s equations. Those are too heavy for computer graphics thus we work with (1) geometrical optics approximations and (2) special case which is can be simplified and used in graphics for material modeling.
- Perfectly planar (optically flat, perfectly smooth) surface* between two homogeneous materials with different index of refraction is starting point for describing the behavior of light interaction with surface. This special case is described with Fresnel's equations:
  - Light falling on such surface can: reflect and refract
  - Amount and directions of light depend on index of refraction
<IMAGE: REFLECTION AND REFRACTION>
* Surface should be infinetly large, but in comparison with wavelenght of light, surface real objects can be considered as such.

---
Reflection on general surfaces
- Real surfaces are not optically flat.
- Often, irregularities are present – larger than wavelength (causing light to reflect differently) and too small to render since this interaction happens under one pixel.
- In this case, we model such surface as a large collection of tiny optically flat surfaces - facets. Final appearance is aggregate result of relevant facets.
  - Smaller deviation of those facets cause more mirror-like surface reflection (small roughness)
  - Larger deviation of those faces causes more blurred surface reflection (glossy, high roughness)
<IMAGE: variation of facets and roughness>

---
Foundations of materials: refraction
- Besides of reflection on surface, light can also refract.
- Amount and direction of refracted light depends on material which we can separate in:
  - Metals
  - Dielectrics
- In case of metals, most of the light is reflected and rest is immediately absorbed. That is why mirrors are made using metal foundation.
- In case of dielectrics, light partially reflects and partially refracts. Refracted light is then absorbed and scattered inside surface (sub-surface scattering*). Some of the light can also be re-emitted – causing diffuse reflection.
<IMAGES: REFLECTION ON METAL AND DIELECTRIC SURFACES>
<IMAGES: real world objects with such properties>
<IMAGE: reflection from metal and dielectric surface: not the color of reflection!>s
* Note that in this case, light is not exiting from the same point where it has entered, thus we need more than local information for calculating light behavior. Therefore, this is one of more complex effects that require advanced rendering methods or approximation methods.

---
Notes on material
- In graphics material is used to describe light-matter interaction. It is a model of a real-world. Note that “material” in graphics encapsulates bit more then just chemical property (which might be the common conception we have about term material) – in graphics it also defines small scale geometrical information that is simply too expensive to represent using actual geometry and shape.
- Based on previous discussion we can see that material can be decomposed and describes both:
  - Scale of geometrical information that is too small to represent explicitly by geometry/shape. Note that most important geometrical information in graphics is normal. For smaller scales, we will describe smaller surfaces thus smaller normals.
  - Substance information encapsulating information on absorption that is color and intensity which will be reflected
<IMAGE: SUBSTANCE OF GLASS AND SMALL SCALE GEOMETRICAL INFORMATION OF GLASS>

---
Surface material representations in 3D scene
- To simplify and understand modeling of 3D object, we separated 3D object in shape and material.
  - By material we mean characteristics of object independent of shape and position. For example, aluminum sphere and aluminum statue – in both cases aluminum properties are the same. Also, changing position of aluminum sphere in space doesn’t change aluminum properties.
  - This enables us to model material separately from shape and its position, since it is enough to model how one tiny bit of material interacts with light and reuse this knowledge at other points.
  - Having same description of material for each point of the 3D object, we would end up with homogeneous material. Therefore, we create parameterized material models and associate some parameters to each point of the surface. For example, this way, we can model marble which has color variation over surface.
- By Material modeling we describe how light should behave when it interacts with objects. For now we will limit our discussion to light interaction with surfaces, and leave light interaction with volume for later.
- Description of light interaction with surface, when considered locally, is called scattering. Once we have a scattering model, we can parameterize it and vary its properties over the surface.
- Shading step in rendering takes material information (alongside with viewing position, object shape and light information on the object) to calculate the object appearance → object color
- Based on discussion above, we can separate material in:
  - Scattering → description of light-matter interaction in a point
  - Texture → variation of scattering function properties across 3D object

---
Example: importance of texture
Show objects with and without texture: texture is variation of scattering model parameters

---
Scattering models

---
Material: scattering function
- We already know that surface orientation (normal) is important shading information since it gives us fundamental information of object appearance – how much is lit.
- How light scatters when it falls on surface point is defined by scattering function which takes in account the normal in this point.
- Scattering function can be separated in reflection and refraction. For now we will focus on reflection. Such scattering function is generally called “bidirectional reflectance distribution function” – BRDF. Defining this function is fundamental and core part of shading process in rendering.
<IMAGE OF BRDF AND ITS ELEMENTS>

---
Note: two faces of BRDF
- BRDF has the name “bidirectional”. This means that given given incoming and outgoing direction, we can compute amount of reflected light in outgoing direction.
- Incoming and outgoing directions can be viewed in two ways:
  - If light is falling on the surface, what is the distribution of reflected light directions (lobe of directions) – this information is particularly useful for ray-tracing (light transport element) as we will see later.
  - If we are looking at the surface from particular direction, how much light will be reflected in this direciton.
<IMAGES: 2 WAYS HOW BRDF CAN BE VIEWED>
<FIND THE BOOK DISCUSSING THIS! Advanced global illumination book?>

---
Types of scattering
- Reflective – all light is scattered above surface
- Transmissive – all light is scattered below surface
  - Refractive – special case of transmissive
- Mirror-like (specular) – light is scattered in single direction (mirror-reflection direction). Perfectly sharp. Dependent of viewing direction.
  - Generally, impulse scattering is term when light is scattered in single direction, but not necessary mirror-reflection direction
- Glossy – scattered light is concentrated around particular direction (lobe). Appears blurred. Dependent of viewing direction.
- Diffuse – light is scattered in all possible directions. Independent of viewing direction. Equally bright from all directions.
- Retro-reflective – scattered light is particularly large when viewing and light directions are close
TODO: IMAGES OF NORMAL AND LIGHT REFLECTION TYPES WITH REAL WORLD IMAGES
TODO: BLENDER EXAMPLE OF BASIC SCATTERING FUNCTIONS

---
Scattering models
- In graphics, various scattering models have been developed (and still are!) to represent surface even more correctly or efficiently. R&D approaches can be classified in: empirical, data-based and physically-based
- Choice of the model depends on application and what is trying to be achieved.
- Practical tips:
  - When modeling a material in DCC Tool, you will be often offered with multiple implementations of basic (or more advanced) models that you further combine to achieve desired material description. In this case, it is good that you are familiar with how they work and their parameters because a lot of time is actually spent on “tweaking” parameters to achieve desired appearance. Understanding parameters of scattering models help very much with upcoming topic: texturing. This is huge and important topic.
  - If you are more interested in developing your own scattering models to achieve different appearance (not necessary photo-realistic, rather non-photorealistic which will be discussed later) then understanding of existing scattering models is great foundation to build on: you will see that advancements of scattering models just added more complexity to basic ones.

---
Basis and scattering function
- On the different scattering types we have seen that they always require normal around which scattering is computed
- Normal defines so called basis
  - <IMAGE>
- Note that perturbing the bases can be constructed using geometrical (object shape) normal. So what would happen if we would somehow vary this normal across smooth shape which has constant geometrical normal? More on this will come when we introduce textures!

---
Scattering models
- Main types are:
  - Empirical
  - Data-based
  - Physical-based

---
Empirical models
- Discuss the way of modeling: by observation, phenomenological approach
- Discuss importance of normal, light position and viewing position.
- Mirror: TODO
- Lambertian: TODO
- Phong and Blinn-Phong: TODO
- Discuss parameters

---
Data-based models
Discuss measurements need for those models

---
Physically-based models
- Highlight importance of normal on different scales
- Reflectance model is half substance information half meso and micro geometry information!
- Microfacets*
* just announce, details in “More on 3D scene modeling”

---
Scattering model parameters
- Scattering models are parameterized.
- Parameters can be mainly decomposed in geometrical and substance
  - Geometrical: roughness, basis normal
  - Substance: color
- Uniform parameters result in overly smooth and perfect surface – not realistic.
- Variation of parameters is done using texturing
<IMAGE: variation of scattering parameters>

---
Texture

---
Variation of material over surface
- Real objects rarely have only one material or material with same properties in each point.
  - Let’s consider wood. Wood has structural texture (e.g., grain) at a scale of about 1mm. Also it has cellular texture at lower scale. The material of wood fiber is different. Therefore, the rich appearance of wood comes from material variation of fibers. This richness is called texture.
- By now, we have seen homogeneous description of material using scattering functions. And objects looks too perfect (too smooth and artificial).
- In order to obtain variation of material across surface (spatial variation) we can vary scattering functions or its properties over it. One material parameter is color. In graphics, we use texture function to vary material properties over surface.
<IMAGES OF HOMOGENEOUS MATERIAL AND MATERIAL WITH VARIATION>
<EXAMPLE IN BLENDER WITH AND WITHOUT TEXTURES>
<EXAMPLES:> https://www.realtimerendering.com/#texture

---
Texture and texture function
- Term texture is used in various disciplines and everyday life: texture of fabric, texture of food, texture in music, texture in image processing, texture in...
- Texture doesn’t have well established definition. It means differently in different disciplines. It spans over multiple scales and over space. But, for our purposes of 3D modeling, we can try to define it as variation of material properties over surface. Therefore, a texture is something that we can completely define and model.
- Texture model is used alongside scattering model during shading rendering step to calculate color of surface in each point. Looking in the rendered image, we will perceive texture on the surface.
  - Note that color of texture in most cases (especially in physically based rendering) is not one on one in the rendered image. Texture merely defines properties of scattering function which is used in rendering process.
  - Note the difference in texture function and texture. Texture is generally overloaded term and it is furthermore overloaded in computer graphics as we will see.
<IMAGE: IMAGE TEXTURE AND RENDERED OBJECT WITH TEXTURE>

---
Texturing: practical example
- Surface texture is its look and feel
  - Bark of a tree, surface of stones, oil painting, etc.
  - <IMAGE>
- In computer graphics, texturing is process that takes surface* and modifies its appearance at each location using image, function or other data source.
  - <IMAGE FOR INTUITION>
    - Texture is property of object
    - During rendering texture is obtained for each point of object
3D scene
Rendering
Object
Shape
Material
Texture
BRDF
* Or volume. For example, variation of gas density can be defined using texture.

---
Texturing: practical example
- Texture is often used to add more details* to the surface.
  - <example>
    - Tree trunk: (1) model shape using cylinder, (2) add color image to add variation (3) add roughness to vary reflection (4) add normal map to break flatness (5) add displacement map to break illusion of normal map
* Remember that computer graphics is all about simulation and approximation in order to achieve required appearance. It is a trade-off between quality and speed. Depending on viewing distance and size of objects in 3D scene, some details can be represented with lower quality. For example, modeling all details on geometrical (shape) level can be very expensive. Thus, texturing come in which represent cheaper way to model details.

---
Texturing: variation
- In previous examples we have seen problems that are solved with textures:
  - Color variation
  - Roughness variation
  - Shading normal variation
  - Geometry variation
- Note that those are exactly parameters of scattering models!
  - Some of those describe variation on small scale: microscale
  - Some of those describe variation on bigger scale: mesoscale
  - Macroscale is given by the object shape.
- Different algorithms solving those problems with varying complexity (and thus quality) exists.

---
Texturing pipeline*
Object space location
Projector function
- Texturing: variation of scattering/shading** parameters over surface – position dependent
- Location in space of object surface/volume
  - Often, object-space locations are used so that is object moves, texture stays the same
- Projection function.
  - This function maps location in object space into location in texture space → texture coordinates
  - This process is called mapping and thus texture mapping (and sometimes texture image is called texture map which is not strictly correct)
- Corresponder function
  - Transform texture coordinates in texture space locations
  - For image texture, this might be indices to retrieve pixel values
  - For procedural texture, this might be domain of procedural function
- Obtaining texture values (sampling)
  - Texture space location is used for reading image texture or evaluating procedural texture
- Value transform
  - If needed additional transformations are done on value that is obtained from texture
- Usage
  - Final value is used to modify property of surface at that point: scattering function parameter or normal.
Texture coordinate
Corresponder function
Texture space location
Texture obtain
Texture value
Value transform
Transformed value
* Note that all steps do not have to be used in different applications!
** Value of texture is used for shading to obtain the final color

---
Texturing pipeline: example
- Wooden floor
  - During rendering, object position (x,y,z) on wooden floor is found
  - Projector function finds mapping from (x,y,z) to (u,v). In this case simple projection can be used: u~=x, v~=y so that u,v are in [0,1] – texture coordinates
  - Corresponder function uses texture coordinates for finding corresponding pixel in the image of wooden floor. If image has resolution 1024x1024 then pixel positions are integer of 1024*u, 1024*v
  - Texture reading is performed using texture space locations
  - Finally, color encoded in texture can not be directly used for rendering, transformation on values is done (e.g., sRBG → linear). Resulting values are used.
  - <ILLUSTRATE>

---
Projector function
- First step in texturing process:
  - Obtaining surface location (given by renderer)
  - Projecting surface location into texture coordinate space (often, but not always, 2D space (u,v)).
- Texture coordinates can be calculated:
  - On the fly during rendering or
  - During object modeling and stored per-vertex – Modeling packages allow artists to edit (u,v) coordinates.
- Many possible ways of obtaining texture coordinates exists:
  - Texture projections
  - Mesh unwrapping

---
Projector function: mesh unwrapping
- Objects are, often, surfaces in 3D space. Image texture lives in 2D space.
- Mesh unwrapping tries to “unwrap” 3D surface onto 2D space.
  - Analogy: world globe and world atlas
- Different methods exists. Unwrapping belongs to larger field called mesh parametrization
  - TODO
- <Example of mesh unwrapping>
- Modeling packages offer different methods for unwrapping and a way to manually enhance the results
  - Goal is that each polygon gets fair share of texture area (e.g., evade stretching) but mantaining connectivity – which determines where separate parts of texture meet and visible seams.
  - EXAMPLE

---
Projector function: texture projection
- The goal is to transform 3D point in space into texture coordinate*
- Commonly used methods in modeling programs are:
  - Spherical
  - Cylindrical
  - Planar
  - <EXAMPLES>
- For highly complex shapes, separating into simpler shapes can be done and then texture projection can be done separately.
<EXAMPLES>
- Spherical projection can be used in environment mapping
- Planar projection uses orthographic projection (usefor for, e.g., decals)
* Note that the goal is really to find texture coordinates and not to find a way of pasting a 2D image on 3D object. This is more general. Once texture coordinates are found, different types of textures can be used: image or procedural, etc.

---
Projector function: texture projection
- Often surface normals are used:
  - This enables triplanar mapping – which of six planar projection directions are used for projecting
  - For curved and tilted surfaces efficient blending of multiple projection planes must be used.
  - EXAMPLE

---
Projector function: different approaches
- Encapsulating object in volume of simpler shapes can make finding texture coordinates more tractable
  - Polycube maps
  - TODO

---
Projector function: different approaches
- View direction can be used for defining projection
  - example
- If object is supplied with any kind of additional information (e.g., curvature or temperature) this can be used for texture coordinate generation
  - Main point is that texture coordinates must be generated in this step. Using position and normal for deriving those is only one way of doing it.

---
Projector function: inherent texture coordinates
- Parametric surfaces have natural set of (u,v) which defines any (x,y,z) point on surface
  - <EXAMPLE>
- In this case, we can say that surface representation already has inherent texture coordinates and projector function is not needed.

---
Projector function: different texture coordinates
- Texture coordinate space doesn’t have to be always 2D
- If texture is used for volumetric objects, then texture coordinates are (u,v,w)
- For animation, texture coordinates can be (u,v,w,t) where t is time and determines change in texture
- Furthermore, procedural texturing can directly rely on object locations – solid texturing.

---
Projector function: different texture coordinates
- Texture coordinate, next to positional, can also be directional
  - Each point in space is accessed by input direction
- Common type of using directional parametrization is cube map
- EXAMPLE

---
Projector function: multiple texture coordinates
- Multiple textures can be applied on objects and thus multiple sets of texture coordinates can be applied
- Idea is the same: those texture coordinates are interpolated across surface and used for obtaining texture value
- <example of multiple textures>

---
Corresponder function
- Convert texture coordinates to texture space locations
  - e.g., u,v to pixel index in image
- Corresponder functions:
  - Which part of sub-texture will be used
  - Transformations: rotate, scale, translate, shear or project
  - How image is applied if (u,v) is larger than 1 or smaller than 0: wrap, mirror, clamp, border, repeat, wang tiles, etc.
- TODO

---
Texture values
- Corresponder function gave texture space coordinates
- Those coordinates are used for obtaining texture values:
  - Image textures
  - Procedural textures
- TODO

---
Image textures
- Texture information can be created in form of images:
  - Drawing images
  - Taking photographs
- Once image textures are created, we need to map them on the 3D object:
  - UV parametrization of 3D object
    - Assign texture coordinates to vertices of 3D object
    - Unfold/unwrap surface onto plane
    - Separate object into patches on which texture is applied
    - Paint texture directly on texture
  - Planar mapping
  - Cylindrical mapping
  - Spherical mapping

---
Examples of image textures
- Substance: https://substance3d.adobe.com/assets/allassets?assetType=substanceMaterial&assetType=substanceAtlas&assetType=substanceDecal
- PolyHaven: https://polyhaven.com/textures

---
Procedural textures
- Procedural texturing is based on algorithm which defined values for each point of 3D space or object surface. Examples:
  - Fourier-like synthesis
  - Perlin noise
  - Reaction-diffusion
<IMAGES: PROCEDURAL TEXTURING>
<IMAGES: NODE SYSTEM FOR PROCEDURAL TEXTURING>

---
Material mapping: variation of parameters
- Modify scattering parameters
- Modify scattering basis
  - Bump, normal
  - Parallax
  - Displacement
TODO

---
Texture modeling and texture application
- When we talk about textures in computer graphics, we can separate the work in creating/modeling a texture and applying it. Often, line between these two is blurred.
- Reminder: we said that material modeling (which includes texture) can be performed separately of modeling 3D shape.
  - Creation of texture is often separated of modeling 3D shape and it is done in so called “texture space”.
  - Texture application is process where we “apply” texture on a 3D shape. That is, map it from texture to object space.
- Texture modeling can be described as process of developing a function which maps some property to each point of the surface. Texture modeling can be separated into:
  - Creating image textures
  - Creating procedural textures
- Texture application can be described as a process of adding actual texture on the object.
  - Often, term texture mapping is used. This term is due to historical reasons where details were painted on 3D model and those details were stored in array of images called textures. The process of corresponding each vertex of model to a location in image was called mapping.
  - Main task in texture application is to find mapping between texture and object space.
- Texture, simply speaking, contains information about surface details. It can be color (albedo), normals, roughness, etc.

---
Storing and transferring materials
- Similarly to mesh information, standards for material storage and transfer are defined
- Material standards:
  - MaterialX
- Certain formats that we mentioned for mesh storage are used for storing the whole scene including the material:
  - GLTF, USD

---
Practical insights

---
Show how is material generated in practice using different scattering functions and textures

---
Literature
- https://github.com/lorentzo/IntroductionToComputerGraphics/wiki/Foundations-of-3D-scene-modeling