Graphics rendering pipeline – logical model of GPU

---
Pipeline abstraction
- Functional/conceptual stages – task to be performed but not how
  - Physical/Implemented stages – how are functional stages implemented in hardware and exposed to the user as API.
Logical model of GPU – exposed to a programmer by API. Physical model is up to the hardware vendor.

---
Graphics rendering pipeline overview
Graphics rendering pipeline
Application
Geometry processing
Rasterization
Pixel processing
Merging
Application
Vertex
shader
Tessellation
Geometry
shader
Clipping
Screen mapping
Triangle setup
Pixel shader
Triangle
 traversial
(Optional)
(Optional)
Compute shader
Programmable
- Conceptual/functional abstraction
Configurable
- Logical model of GPU - API
Fixed

---
GPU graphics rendering pipeline
GPU implements conceptual rendering pipeline

---
GPU graphics rendering pipeline
- Logical model is exposed to used as API
  - Underlaying hardware implementation varies by hardware vendor (e.g., Nvidia, AMD, Intel, etc.)

---
Programming a GPU renderer
- As programmers, we are interested in:
  - Application stage
  - GPU programmable and configurable stages: vertex shader, pixel shader, screen mapping and merger
CPU
GPU
Application
Programmable
Configurable
Fixed

---
Programming a GPU renderer
- Unified shader design: vertex, pixel, geometry, tessellation shaders share common programming model – same instruction set arhitecture (ISA)
- GPU with cores which supports unified shader design: unified shader architecture

---
Programming a GPU renderer
- Application stage can be written in various languages:
  - C, C++
  - Python
  - Rust
  - etc.
- Different APIs enable GPU rendering:
  - OpenGL (cross-platform), OpenGL shading language (GLSL)
  - DirectX (Windows), High-level shading language (HLSL)
  - Vulkan (cross-platform)
  - Metal (iOS)

---
Programming a GPU renderer
- Parameters and states of graphics API are defined on application stage
- Draw call invokes graphics API to draw primitives
  - Causing graphics pipeline to execute and run its shaders
- Programmable shaders have two types of inputs:
  - Uniform inputs: values remain the same through draw call, e.g., transformation matrix of static object, color of light source, texture, etc.
  - Varying inputs: data that come from triangle vertices or rasterization, e.g., triangle surface location changes per pixel

---
Shading languages
- Vertex, geometry, tessellation shader
  - Enables programming of geometry behaviour
- Fragment shader
  - Enables programming material models, light interaction, post-processing effects
- Shading languages support common graphics computations:
  - Additions, multiplications, etc.
  - Intrinsic functions: cos(), atan(), log(), etc.
  - Complex operations: vector normalization, reflection, cross product, matrix operations, etc.
  - Flow control on uniforms (static flow control) and varyings (dynamic control flow)

---
Evolution of graphics API and hardware
https://www.realtimerendering.com/

---
Graphics rendering pipeline – OpenGL demo

---
OpenGL rendering pipeline
- Application stage
- Vertex shader
- Fragment shader
Application

---
Application stage
TODO
- Define:
  - Camera
  - Light
  - Object: geometry and material
  - Shader parameters
  - Configurable GPU pipeline parameters
- Draw call
https://learnopengl.com/code_viewer_gh.php?code=src/2.lighting/2.2.basic_lighting_specular/basic_lighting_specular.cpp

---
Application stage: camera
TODO
- Resolution
- Position, orientation
  - View and projection matrix

---
Application stage: light
TODO
- Point light:
  - Position
  - Color

---
Application stage: object
TODO

---
Application stage: shader programs
TODO
Shader parameters

---
Application stage: pipeline state
TODO

---
Application stage: whole
TODO
https://learnopengl.com/code_viewer_gh.php?code=src/2.lighting/2.2.basic_lighting_specular/basic_lighting_specular.cpp

---
Vertex shader
TODO
https://learnopengl.com/code_viewer_gh.php?code=src/2.lighting/2.2.basic_lighting_specular/2.2.basic_lighting.vs

---
Fragment shader
TODO
https://learnopengl.com/code_viewer_gh.php?code=src/2.lighting/2.2.basic_lighting_specular/2.2.basic_lighting.fs

---
Output
TODO